## Slide 1: W.I.L.D. Wilderness Information Link Device
Group 10
Brandyn Brinston - CpE
Caleb Phillips - CpE
MICHAEL SEDLACK - EE & PHYSICS
JUSTIN TUGGLE - EE

## Slide 2: Project Goal Statement and Description
Our goal is to make a small, portable communication device that does not rely on any external network. This device must also be suitable for use in adverse conditions with a high level of reliability.
  Text-based communication
  Battery-powered with solar charging
  Long range (>1 mile)
  Priced competitively to alternatives (satellite phone etc.)

## Slide 3: Project Components
Wireless Module
Power Supply
Input/Output
  Keyboard
  LCD
  Cursor
  Status Indicators
MCU/Software
  Microcontroller
  Keyboard input
  LCD output

## Slide 4: Hardware Block Diagram
Power Supply
Transceiver
MCU
Display
Keyboard
Status Indicators
I/O
Legends:
Brandyn
Caleb
Michael
Justin
Data
Power

## Slide 5: Project Components
Wireless Module
Power Supply
Input/Output
  Keyboard
  LCD
  Cursor
  Status Indicators
MCU/Software
  Microcontroller
  Keyboard input
  LCD output

## Slide 6: Wireless Communications
XBee (Pro) SX
  Maximum range of up to 50 miles
  Power usage of 1 watt or less
  Cost within project constraints
  Capable of peer-to-peer and mesh networks
  Built-in data encryption and packet acknowledgment
  Conforms to federal power and bandwidth regulations (902-928Mhz, FCC §15.247)
  Support for multiple antenna formats (u.fl and RF pad)

## Slide 7: Project Components
Wireless Module
Power Supply
Input/Output
  Keyboard
  LCD
  Cursor
  Status Indicators
MCU/Software
  Microcontroller
  Keyboard input
  LCD output

## Slide 8: Power Supply Specifications
High efficiency (preferably > 75% from battery to voltage rails)
Single 3.3-volt rail, capable of 1.5A current capacity
Sufficient decoupling to avoid supply sag
Ability to charge 4.2-volt Li-Ion battery from USB and solar
Power Supply Revision 1 - PCB
Power Supply Revision 1 - Populated

## Slide 9: Power Supply Schematic

## Slide 10: Power Supply PCB
Power Supply Revision 2 PCB - Top
Power Supply Revision 2 PCB - Bottom
1.225”
1.160”

## Slide 11: Testing – Power Supply
Confirmed that both USB and solar inputs accept power and attempt to charge the battery
Confirmed that 3.3-volt rail provides a very steady voltage without load
Need to test charge/discharge cycles
Need to confirm that voltage rail remains steady with changing load
3.3-volt rail tested with a battery

## Slide 12: Project Components
Wireless Module
Power Supply
Input/Output
  Keyboard
  LCD
  Cursor
  Status Indicators
MCU/Software
  Microcontroller
  Keyboard input
  LCD output

## Slide 13: Main Input Device Considerations
T9-configuration (predictive text, 9 keys, i.e telephone keypad)
Cursor
QWERTY Keyboard
  This type of configuration seemed ideal, as it would give users the easiest means of inputting characters whilst saving time
  Considered PCB design or using a pre-made device
  Complications for design based off mechanical specs i.e. the dimensions set

## Slide 14: BlackBerry Q10 Module
Operates at 3.3V
Contains backlighting for keys, with a driving current of 40 mA for max brightness
Ergonomically designed for ease and comfort for users when typing
35 regular character inputs, 28 specials
7 Rows x 5 Columns matrix
I2C interfacing

## Slide 15: Keyboard Connector (Hirose BM14B)
Rated for 30V, 300 mA
0.4 mm Pitch
28 Conductors
5.842 mm x 2.794 mm x 0.8 mm
Breakout board designed for I/O prototyping

## Slide 16: Hardware Testing for Q10
Flex cable properly connects to BM14B
Backlighting for keys successfully turn on once voltage is supplied
Potential displays a change in voltage when a key is pressed

## Slide 17: LCD Module (ERM2004-2)
Operates at 3.3V
Backlighting requires 45 mA
20 Char x 4 Line display
16 pin header
8-bit parallel data lines for interfacing, operable in 4-bit mode
Support for custom characters
A menu will be incorporated for the display, containing a variety of option for the user, such as power settings, message pages and device information.

## Slide 18: Cursor Input Module (SKQUCAA010)
Practical solution for ease of interfacing and menu navigation
Operates at 1V-12V, 10μA – 50 mA
Five-way directional input (forward, backward, left, right, down)
20.8 mm x 10.67 mm
Another breakout board designed for prototyping purposes

## Slide 19: Status Indicators
RGB LEDs will be used as a means of notifying users into the status of messages
Typical 3mm LEDs will be used in a biasing circuit for testing stages of design code
Color coding will be used in conjunction with the various standings/progress of the message
Implementation of MOSFET transistors along with PWM will be necessary in order to make various colors i.e orange, yellow, purple etc.

## Slide 20: Project Components
Wireless Module
Power Supply
Input/Output
  Keyboard
  LCD
  Cursor
  Status Indicators
MCU/Software
  Microcontroller
  Keyboard input
  LCD output

## Slide 21: Keyboard Software
• Each column and row corresponds to GPIO pin on MCU
• Row pins set to 1, column pins set to 0
• On key press, row pins read low output
•‘If statements’ used to check pin output
• Once condition met, character or symbol is determined
Keyboard Characters, Symbols, and Numbers

## Slide 22: Keyboard Software
Keyboard and Display Software Diagram

## Slide 23: MCU Selection
Microcontroller | Architecture | Clock | Storage/RAM | UART | SPI | I2C | ADC Channels | GPIO Pins
ATmega1284P | 8-bit | 20 MHz | 128KB / 16KB | 2 | 3 | 1 | 8 | 32
MSP430FR5964 | 16-bit | 16 MHz | 256KB / 8KB | 4 | 8 | 4 | 20 | 68
MSP432P401R | 32-bit | 48 MHz | 256KB / 64KB | 4 | 8 | 4 | 24 | 84

## Slide 24: MCU: MSP432P401R
ARM Architecture
  Energy Efficient
  Low Power
  Low Cost
MCU | Total Power Saving Modes | Active Mode Current Consumption
ATmega1284P | 6 | 320 μA
MSP430FR5964 | 4 | 118 μA
MSP432P401R | 6 | 80 μA
MCU | Cost
ATmega1284P | $ 5.29
MSP430FR5964 | $ 6.45
MSP432P401R | $ 7.46

## Slide 25: MCU: MSP432P401R
TI Familiarity
  Well Documented
  Comprehensive Support and Training
MSP432P401R
MSP432P401R Development Board

## Slide 26: Project Progress

## Slide 27: Financing
Item | Quantity | Money Spent | Money Budgeted
XBee Developer kit | 1 | $249 | 
XBee Chips | 2 | $189 | 
Displays | 3 | $47 | 
Keyboards | 3 | $5 | $10
MSP432 Debugging Kit | 1 | $99 | 
Microcontrollers | 3 | $35 | 
PCBs | 2+3 | $90 | $50
Board Components & Misc. | NA | $35 | 
Batteries | 3 | $10 | $20
Case Printing | 3 |  | $50
Solar Panels | 3 |  | $50
Administrative Docs | 2 | $30 | $30
 |  | Total: $789 | Total: $210
Chart: Total Funds ($1100)
| Spent | Budgeted | Unallocated
Total Funds($1000) | 789 | 210 | 101

## Slide 28: Potential Challenges
Soldering small components on crowded boards
Layout of antenna connection on PCB board
Design and fitting of device case
Finding libraries to restrict amount of code stored in MCU—specifically with UI
Potential compatibility issues between separate modules.

## Slide 29: Team Contributions
Name: | Power | I/O | PCB Design | Keyboard Code | LCD Code | XBee Code | UI Code
Brandyn |  |  |  | Primary | Secondary | Secondary | Primary
Caleb |  | Tertiary |  | Secondary | Primary | Primary | Secondary
Michael | Primary | Secondary | Primary | Tertiary |  |  | 
Justin | Secondary | Primary | Primary |  |  |  | 

## Slide 30: Remaining Milestones
Week 7 | Test PSU revision 2 Design MOSFET-controlled LED biasing circuit Continue software development
Week 8 | Prepare to learn mechanical drawing software, design enclosure Software beta complete
Week 9 | Design MCU PCB & solder relevant components Test breadboard prototype
Week 10 | Testing and revisions
Week 11 | Finish design of prototype model, look into potential improvements
Week 12 | Verify functionality of devices, and prepare for committee presentation

## Slide 31: Questions?