## Slide 1: W.I.L.D. Wilderness Information Link Device
Group 10
Brandyn Brinston - CpE
Caleb Phillips - CpE
MICHAEL SEDLACK - EE & PHYSICS
JUSTIN TUGGLE - EE

## Slide 2: Project Goal Statement and Description
Our goal was to make a small, portable communication device that does not rely on any external network. The goals of this device were to be suitable for use in adverse conditions with a high level of reliability.
  Text-based communication
  Battery-powered with solar charging
  Long range (>1 mile)

## Slide 3: Project Components
Wireless Module
Input/Output
  Keyboard
  LCD
  Cursor
  Status Indicators
  Enclosure
MCU/Software
  Microcontroller
  Keyboard input
  LCD output
Power Supply and Mainboard

## Slide 4: Hardware Block Diagram
Power Supply
Transceiver
MCU
Display
Keyboard
Status Indicators
I/O
Legends:
Brandyn
Caleb
Michael
Justin
Data
Power

## Slide 5: Project Components
Wireless Module
Input/Output
  Keyboard
  LCD
  Cursor
  Status Indicators
  Enclosure
MCU/Software
  Microcontroller
  Keyboard input
  LCD output
Power Supply and Mainboard

## Slide 6: Wireless Communications
XBee (Pro) SX
  Maximum range of up to 50 miles
  Power usage of 1 watt or less
  Cost within project constraints
  Capable of peer-to-peer and mesh networks
  Built-in data encryption and packet acknowledgment
  Conforms to federal power and bandwidth regulations (902-928Mhz, FCC §15.247)
  Support for multiple antenna formats (u.fl and RF pad)

## Slide 7: Project Components
Wireless Module
Input/Output
  Keyboard
  LCD
  Cursor
  Status Indicators
  Enclosure
MCU/Software
  Microcontroller
  Keyboard input
  LCD output
Power Supply and Mainboard

## Slide 8: Main Input Device Considerations
T9-configuration (predictive text, 9 keys, i.e telephone keypad)
Cursor
QWERTY Keyboard
  This type of configuration seemed ideal, as it would give users the easiest means of inputting characters whilst saving time
  Considered PCB design or using a pre-made device
  Complications for design based off mechanical specs i.e. the dimensions set

## Slide 9: BlackBerry Q10 Module
Operates at 3.3V
Contains backlighting for keys, with a driving current of 40 mA for max brightness
Ergonomically designed for ease and comfort for users when typing
35 regular character inputs, 28 specials
7 Rows x 5 Columns matrix
I2C interfacing

## Slide 10: Keyboard Connector (Hirose BM14B)
Rated for 30V, 300 mA
0.4 mm Pitch
28 Conductors
5.842 mm x 2.794 mm x 0.8 mm
Breakout board designed for I/O prototyping

## Slide 11: Hardware Testing for Q10
Flex cable properly connects to BM14B
Backlighting for keys successfully turn on once voltage is supplied
Potential displays a change in voltage when a key is pressed

## Slide 12: LCD Module (ERM2004-2)
Operates at 3.3V
Backlighting requires 45 mA
20 Char x 4 Line display
16 pin header
8-bit parallel data lines for interfacing, operable in 4-bit mode
Support for custom characters
A menu will be incorporated for the display, containing a variety of option for the user, such as power settings, message pages and device information.

## Slide 13: Cursor Input Module (SKQUCAA010)
Practical solution for ease of interfacing and menu navigation
Operates at 1V-12V, 10μA – 50 mA
Five-way directional input (forward, backward, left, right, down)
20.8 mm x 10.67 mm
Another breakout board designed for prototyping purposes

## Slide 14: Status Indicators
RGB LEDs will be used as a means of notifying users into the status of messages
Typical 3mm LEDs will be used in a biasing circuit for testing stages of design code
Color coding will be used in conjunction with the various standings/progress of the message
Implementation of MOSFET transistors along with PWM will be necessary in order to make various colors i.e orange, yellow, purple etc.

## Slide 15: Enclosure
Dimensions are 5.8 in x 5.3 in x 1.635 in
Material is ABS plastic
Mechanical specifications of each component used as basis for cutouts
Designed in Autodesk Fusion 360

## Slide 16: Project Components
Wireless Module
Input/Output
  Keyboard
  LCD
  Cursor
  Status Indicators
  Enclosure
MCU/Software
  Microcontroller
  Keyboard input
  LCD output
Power Supply and Mainboard

## Slide 17: Keyboard Software
• Each column and row corresponds to GPIO pin on MCU
• Row pins set to 1, column pins set to 0
• On key press, row pins read low output
•‘If statements’ used to check pin output
• Once condition met, character or symbol is determined
Keyboard Characters, Symbols, and Numbers

## Slide 18: Keyboard Software
Keyboard and Display Software Diagram

## Slide 19: MCU Selection
Microcontroller | Architecture | Clock | Storage/RAM | UART | SPI | I2C | ADC Channels | GPIO Pins
ATmega1284P | 8-bit | 20 MHz | 128KB / 16KB | 2 | 3 | 1 | 8 | 32
MSP430FR5964 | 16-bit | 16 MHz | 256KB / 8KB | 4 | 8 | 4 | 20 | 68
MSP432P401R | 32-bit | 48 MHz | 256KB / 64KB | 4 | 8 | 4 | 24 | 84

## Slide 20: MCU: MSP432P401R
ARM Architecture
  Energy Efficient
  Low Power
  Low Cost
MCU | Total Power Saving Modes | Active Mode Current Consumption
ATmega1284P | 6 | 320 μA
MSP430FR5964 | 4 | 118 μA
MSP432P401R | 6 | 80 μA
MCU | Cost
ATmega1284P | $ 5.29
MSP430FR5964 | $ 6.45
MSP432P401R | $ 7.46

## Slide 21: MCU: MSP432P401R
TI Familiarity
  Well Documented
  Comprehensive Support and Training
MSP432P401R
MSP432P401R Development Board

## Slide 22: Project Components
Wireless Module
Input/Output
  Keyboard
  LCD
  Cursor
  Status Indicators
  Enclosure
MCU/Software
  Microcontroller
  Keyboard input
  LCD output
Power Supply and Mainboard

## Slide 23: Mainboard Specifications
Provide all necessary support hardware for selected MCU
Provide connections for all device I/O
Compact enough to fit inside reasonably-sized case
Modular as possible to ease in prototyping and assembly
Top of Mainboard

## Slide 24: Mainboard Schematic

## Slide 25: Mainboard PCB
Mainboard PCB - Top
Mainboard PCB - Bottom
2.04”
2.04”

## Slide 26: Power Supply Specifications
High efficiency (preferably > 75% from battery to voltage rails)
Single 3.3-volt rail, capable of 1.5A current capacity
Sufficient decoupling to avoid supply sag
Ability to charge 4.2-volt Li-Ion battery from USB and solar
Power Supply Revision 2

## Slide 27: Power Supply Schematic

## Slide 28: Power Supply PCB
Power Supply Revision 2 PCB - Top
Power Supply Revision 2 PCB - Bottom
1.225”
1.160”

## Slide 29: Testing – Power Supply
Confirmed that both USB and solar inputs accept power and attempt to charge the battery
Confirmed that 3.3-volt rail provides a very steady voltage without load
Confirmed that voltage rail remains steady with changing load
3.3-volt rail tested with a battery

## Slide 30: Project Progress

## Slide 31: Financing
Item | Quantity | Money Spent
XBee Developer kit | 1 | $249
XBee Chips | 2 | $189
Displays | 3 | $47
Keyboards | 3 | $15
MSP432 Debugging Kit | 1 | $99
Microcontrollers | 3 | $35
PCBs | 2+3 | $140
Board Components & Misc. | NA | $35
Batteries | 3 | $30
Case Printing | 3 | $50
Solar Panels | 3 | $50
Administrative Docs | 2 | $30
 |  | Total: $1070

## Slide 32: Team Contributions
Name: | Power | I/O | PCB Design | Keyboard Code | LCD Code | XBee Code | UI Code
Brandyn |  |  |  | Primary | Secondary | Secondary | Primary
Caleb |  | Tertiary |  | Secondary | Primary | Primary | Secondary
Michael | Primary | Secondary | Primary | Tertiary |  |  | 
Justin | Secondary | Primary | Primary |  |  |  | 

## Slide 33: Challenges
Soldering small components on crowded boards
Difficulty working with keyboard connector
Layout of antenna connection on PCB board
Design and fitting of device case
Finding libraries to restrict amount of code stored in MCU—specifically with UI

## Slide 34: If we had more time…
Fully functional secondary module
Alternative keyboard option
Direct addressing when sending message
More options to device/more robust UI
More onscreen information; such as displaying current charge

## Slide 35: Demonstration